## Slide 1: DMC-CFA Workshop ARENA Hands-on Experience
Team members: Cheng Tan, Chenhao Xie,
Tong Geng, Ang Li (PI)
Notes: Image: Abstract Data Visualization – Stock Photo

## Slide 2: ARENA: Asynchronous Reconfigurable Accelerator Ring for the Next Generation HPC Clusters
Background
System architecture
Programming model
Evaluation
Tutorial

## Slide 3: Background – Abstract Machine Model (AMM)

## Slide 4: Background – Abstract Machine Model (AMM)
1. More heterogeneity
2. Shared memory
3. System-on-chip via NoC

## Slide 5: Background – Abstract Machine Model (AMM)
1. More heterogeneity
2. Shared memory
3. System-on-chip via NoC
1. Reconfigurability
2. Synchronous process-based vs. asynchronized task-based
3. Compute-flow architecture
Notes: 1. Conventional is synchronous process-based model vs. asynchronous task-based.

## Slide 6: Background – Motivating Example
Conventional compute-centric vs. data-centric execution

## Slide 7: Background – Motivating Example
(d) ARENA’s data-centric with dynamic reconfigurable acceleration
Conventional compute-centric vs. data-centric execution
Reducing non-essential data movement

## Slide 8: System Architecture
Overview
Micro-architecture of ARENA node
Software/hardware implementations

## Slide 9: Overview of ARENA
Task token delivered in the ring
Task dispatcher
NIC
CGRA/FPGA or CPU

## Slide 10: Overview of ARENA
Task token delivered in the ring
Task dispatcher
NIC
CGRA/FPGA or CPU

## Slide 11: Overview of ARENA
Task token delivered in the ring
Task dispatcher
NIC
CGRA/FPGA or CPU

## Slide 12: Micro-Architecture of ARENA Node
Task dispatcher
  Receive Queue
  Send Queue
  Wait Queue
CGRA
  CGRA Controller
  Scratchpad Data Memory
  8x8 Tiles

## Slide 13: Software/Hardware Implementations
Software framework
  Implemented using MPI
  Mimic functionality of dispatcher
  Evaluate execution model
Hardware implementation
  CGRA support
  RTL-based task dispatcher, CGRA, and CGRA controller

## Slide 14: Software/Hardware Implementations
Software framework
  Implemented using MPI
  Mimic functionality of dispatcher
  Evaluate execution model
Hardware implementation
  CGRA support
  RTL-based task dispatcher, CGRA, and CGRA controller

## Slide 15: Programming Model
ARENA runtime

## Slide 16: Programming Model
ARENA runtime

## Slide 17: Programming Model
ARENA runtime

## Slide 18: Programming Model
ARENA runtime

## Slide 19: Programming Model
ARENA runtime

## Slide 20: Programming Model
ARENA runtime

## Slide 21: Programming Model
ARENA runtime

## Slide 22: Programming Model
ARENA runtime
ARENA programming interfaces
  User-defined functions/tasks
  User APIs
  Hardware abstract functions
  Base constructs
ARENA APIs

## Slide 23: Programming Model
ARENA runtime
ARENA programming interfaces
  User-defined functions/tasks
  User APIs
  Hardware abstract functions
  Base constructs
ARENA APIs

## Slide 24: Evaluation
Representative HPC kernels
Simulation environment
  SST + RTL
ARENA’s Data-centric execution model
  Asynchronous task execution
  Reduced data communication
CGRA speedup
  2x8 tiles
  4x8 tiles
  8x8 tiles
Simulation environment

## Slide 25: Evaluation

## Slide 26: Evaluation
Representative HPC kernels
Simulation environment
ARENA’s Data-centric execution model
CGRA speedup
Reduced data communication
ARENA layout (w/o data memory)
https://github.com/pnnl/OpenCGRA
Synthesized by OpenCGRA (SODA^2 + CFA)

## Slide 27: Take-aways
Programming Model Comparison
Cilk
  Fork-join idiom requires synchronization
  No data locality awareness
  Centralized work stealer
MapReduce
  Strict execution model
  No data locality awareness
MPI
  Conventional two-sided communication
  Requires synchronization
OpenSHMEM
  Partitioned Global Address Space (PGAS)
  Implicit massive data movement under the hood

## Slide 28: Take-aways
synch point in Cilk
Data locality awareness in ARENA
Programming Model Comparison
Cilk
  Fork-join idiom requires synchronization
  No data locality awareness
  Centralized work stealer
MapReduce
  Strict execution model
  No data locality awareness
MPI
  Conventional two-sided communication
  Requires synchronization
OpenSHMEM
  Partitioned Global Address Space (PGAS)
  Implicit massive data movement under the hood

## Slide 29: Take-aways
Programming Model Comparison
Cilk
  Fork-join idiom requires synchronization
  No data locality awareness
  Centralized work stealer
MapReduce
  Strict execution model
  No data locality awareness
MPI
  Conventional two-sided communication
  Requires synchronization
OpenSHMEM
  Partitioned Global Address Space (PGAS)
  Implicit massive data movement under the hood
synch point in Cilk
Data locality awareness in ARENA

## Slide 30: Take-aways
Suitable Applications
Graph Applications
  Sparsity/workload imbalance
Monte-Carlo Markov algorithm
  Variable chain length
Molecular Dynamics (MD)/Nbody
  Irregular communication
  Workload imbalance
Reinforcement Learning
  Variable rollout length
Programming Model Comparison
Cilk
  Fork-join idiom requires synchronization
  No data locality awareness
  Centralized work stealer
MapReduce
  Strict execution model
  No data locality awareness
MPI
  Conventional two-sided communication
  Requires synchronization
OpenSHMEM
  Partitioned Global Address Space (PGAS)
  Implicit massive data movement under the hood

## Slide 31: Tutorial
HelloWorld
SSSP
GEMM
GCN (dense/HiCOO)

## Slide 32: Tutorial – HelloWorld
Classic ping-pang problem
What we want to learn:
  Data-centric execution: The data range indicated by a token should match the data range of the specific machine that captures/executes the token.
  A value can be carried by the task token: counter is passed between machines using the ‘PARAM’ indicated by the token.
Data range: 0 ~ 10
Data range: 20 ~ 30
Node 0
Node 1
Token (0~5)
Token (21~25)

## Slide 33: Tutorial – SSSP
Single Source Shortest Path
  Adjacency matrix
What we want to learn:
  Data-centric execution: A graph node is executed by a specific machine where the node resides.
  A value can be carried by the task token: ‘hops’ is passed between machines using the ‘PARAM’ indicated by the token.
∞
0
∞
0
Adjacency Matrix:
`∞` indicates an edge,
`0` indicates no edge
Nodes range: 0 ~ 1
Machine 0
Nodes range: 1 ~ 2
Machine 1
Nodes range: 2 ~ 3
Machine 2
Nodes range: 3 ~ 4
Machine 3
node0
node1
node2
node3

## Slide 34: Tutorial – GEMM
GEMM: ⍺ x A x B + β x C
  A, B’, C are equally distributed
What we want to learn:
  Essential data movement: Transposed matrix B’s rows.
Row range: 0 ~ 1
X
Matrix A
Transposed matrix B
(pipelined delivered on ring)
Machine 0: Row(A1) x Row(B1)

## Slide 35: Tutorial – GEMM
GEMM: ⍺ x A x B + β x C
  A, B’, C are equally distributed
What we want to learn:
  Essential data movement: Transposed matrix B’s rows.
Row range: 0 ~ 1
Row range: 1 ~ 2
X
Matrix A
Machine 0: Row(A1) x Row(B1)
Machine 1: Row(A2) x Row(B1)
Transposed matrix B
(pipelined delivered on ring)

## Slide 36: Other examples -- GCN
Graph Convolutional Network
  Two-layer GCN with CORA dataset
  Main computation: A x X x W
  Dense/HiCOO (HiParTi + CFA)
  Power grid cascading failure prediction (HollonicML + CFA)
Try to include more built-in kernels to ease the programming effort

## Slide 38: ARENA: Asynchronous Reconfigurable Accelerator Ring for the Next Generation HPC Clusters
Cheng Tan, Chenhao Xie, Tong Geng, Andres Marquez, Antonino Tumeo, Kevin Barker, Ang Li
Notes: NOTE: This file must print at 200% SCALE to achieve a final print size of 60” wide x 42” tall.
• Contact Digital Duplicating (375-2969, http://digitalduplicating.pnl.gov) to order poster printing and finishing services for your completed poster design.
• Remember to have your poster cleared for public display/distribution through the Information Release system (https://informationrelease.pnl.gov).

## Slide 39: Tutorial – BFS Kernel
Single source shortest path
Conventional compute-centric model
  Implemented using MPI
  Non-essential data communication
  Synchronization overhead

## Slide 40: Case Study – BFS Kernel
Single source shortest path
Conventional compute-centric model
  Implemented using MPI
  Non-essential data communication
  Synchronization overhead
ARENA’s Data-centric execution model
  Asynchronous task execution
  Reduced data communication